|  | ICEPOD Campaign: AN04 |
| --- | --- |
| FLIGHT REPORT |
| Flight Number: | AN04_F1006 | Line Number: | PIPERS1 & partial ROSETTA L770 |
| Date: | 21 Nov, 2017 (UTC) Tuesday 21 Nov, 2017 PM (local) |
| Prepared by: | Tinto |
| Takeoff time: | 0756 | Land time: | 1301 |
| Duration: | 5.1 hrs |  |

| DATA SUMMARY |
| --- |
| Instrument | Operated | QC | Notes |
| POD-INS (SPAN) | Y | Y |  |
| HATCH-GNSS (LEICA_air) | Y | Y |  |
| DGS-INS | Y | Y |  |
| iMAR-INS | Y | Y |  |
| BASE1 (Leica ground) | N | N |  |
| GRAVITY DgS | Y | Y |  |
| GRAVITY ZLS | Y | Y |  |
| RADAR DICE | Y | Y |  |
| RADAR SIR | Y | Y |  |
| MAG AIR | Y | N | Cs3 failed – Fluxgate functioned normally |
| MAG BASE | Y | Y |  |
| LIDAR | Y | Y | TOWN PASS – fuel tanks look skewed |
| KT15 | Y | - |  |
| BOBCAT | Y | Y |  |
| IRE | Y | Y |  |
| DGU | Y | Y |  |

FLIGHT TRACK

Notes

Preflight

Flown for PIPERS project. Delayed reopening of airfield caused 3-hour delay to takeoff.  Truncated mission planned (5hrs) to take advantage of clear skies in Terra Nova Bay region.  Outbound along previously occupied (2015) IcePod track and inbound along TandemX track from 25 November.

Flight

Clear skies persisted to ~half way through TandemX track at which point course was abandoned.  Travelled home along partial ROSETTA survey line (770).

Postflight

All instruments performed well.

Bobcat: overexposed towards the end of the flight

DICE: only turned on over ice shelf. In flight display saturated but no issues reported from processed data.  Suggested slightly higher flight elevation for next flight.

SPAN: several restarts of the system

Master config: not updating SIR flight number

Magnetometer: Cs3 not working throughout flight.

Lidar: town pass shows skewed image.  “Old” matrix